## Slide 1: Fuzzy Logic Based Image Quality Control in Low Light Situations
Laptop
Arduino
webcam
LED
Student: Chia Sheng Kuo
Adviser: Prof. Chi Cheng Cheng
Dept. of Mechanical and Electro-Mechanical Engineering National Sun Yat-Sen University

## Slide 2: OUTLINE
Brief introduction to AE
System Specification
Input & Output
Environment Test
Fuzzification
Fuzzy Inference
Defuzzification
Result & Conclusion

## Slide 3
Auto Exposure
In low light situation, even AE is applied, image quality could be degraded.
That’s the reason why camera needs the flashlight.

## Slide 4
Specification
Laptop (Visual Studio 2017 + OpenCV 3.4.1)
fuzzylite 6.0
Logitech HD Webcam C310
Arduino UNO Board *2 (5V Output)
LED *30 ( Vf = 3.2V, If = 20mA)
Resistor 30 *6, 47 *6

## Slide 5
Input
Output
Fuzzification
Inference
Defuzzification

## Slide 6
Input & Output of the System
Input | Output
Mean gray value = | PWM Signal Resolution 0 – 255
Input | Output
 | PWM Signal Resolution 0 – 255

## Slide 7
Input
Output
Fuzzification
Inference
Defuzzification
Before fuzzification, the possible range of the input and output should be acquired.

## Slide 8
Red: Environment
Green: Control
Environment:
PWM goes back and forth from 0 to 255.
For example:
Mean gray value
Environment test

## Slide 9
Environment:
PWM goes back and forth from 0 to 255.
For better understanding
The goal is to make the Input signal smooth even though environment is changing non-stop.
Mean gray value
Entropy
SNR

## Slide 10
Upper boundary and lower boundary
Upper boundary:
Environment(When PWM=255) + Control(PWM=255)
Lower boundary:
Environment(When PWM=0) + Control(PWM=0)

## Slide 11
 | Mean gray value | Entropy | SNR | Error | Error rate | PWM
Upper boundary | 164 | 5.22 | 6.53 | ? | ? | 255
Lower boundary | 0 | 0 | -48 | ? | ? | 0
Mathematically, The range of the boundary would be larger the possible.

## Slide 12
Mean gray value
Entropy

## Slide 13
SNR
PWM

## Slide 14
Input
Output
Fuzzification
Inference
Defuzzification
From intuition to PD like fuzzy controller

## Slide 15
If gmean is dark or SNR is poor then PWM is high.
If gmean is dark or entropy is poor then PWM is high.
If SNR is poor or entropy is poor then PWM is high.
If gmean is bright and entropy is excellent then PWM is medium.
If gmean is bright and SNR is excellent then PWM is medium.
If SNR is excellent and entropy is excellent then PWM is medium.
Inference based on intuition:

## Slide 16
Inference based on intuition
Result is not good. Especially for mean gray value
Set point =128
Mean gray value
PD like fuzzy Inference

## Slide 17
 | Mean gray value | Entropy | SNR | Error | Error rate | PWM
Upper boundary | 164 | 5.22 | 6.53 | 40 | 5 | 255
Lower boundary | 0 | 0 | -48 | -20 | -5 | 0
To implement the PD like fuzzy controller, the Error and the Error rate is computed.

## Slide 18
Error
Error rate
PWM

## Slide 19
PD like fuzzy Inference:
 | NL | NS | Z | PS | PL
PL | Z | PS | PM | PL | PL
PS | NS | Z | PS | PM | PL
Z | NM | NS | Z | PS | PM
NS | NL | NM | NS | Z | PS
NL | NL | NL | NM | NS | Z
E
ER

## Slide 20
Input
Output
Fuzzification
Inference
Defuzzification
Inference Method: Mamdani
Conjunction: Minimum
Disjunction: Maximum
Defuzzification Method: Centroid

## Slide 21
One more thing
Error rate
=0.25
3*=0.75
Signal vibrate every 4 frames
2nd order Low pass filter
u(k) = x ER + x u(k-1) - x u(k-2)
Filter
ER

## Slide 22
Input
Output
Fuzzification
Inference
Defuzzification

## Slide 23
Inference based on intuition
PD like fuzzy Inference
Controller Output PWM
110
35

## Slide 24: Result
Mean gray value
Entropy
SNR
Without fuzzy controller
Set point =128

## Slide 25
Mean gray value
Entropy
SNR
Auto Exposure
Set point =128

## Slide 26
Mean gray value
Entropy
SNR
Fuzzy controller
Set point =128

## Slide 27
 | Proposed Method | AE
Fps | 18 | 12
Error | -10 to 16 | 0 to 128
 | Proposed Method | AE
Fps |  | 
Error | -10 to 16 | 0 to 128
Conclusion
Proposed Method is better than AE in low light situation.